| A.B.N. 63 103 035 687 | MECAL PTY. LTD. 9 Paramount Road (P.O. Box 4140) West Footscray Vic 3012 AUSTRALIA Website: www.mecal.com.au | Phone: 03 9314 0144 Fax: 03 9314 2576 Int’l Phone: +61 3 9314 0144 Fax: +61 3 9314 2576 Email: mecal@mecal.com.au |
| --- | --- | --- |

MECAL ‘NO DUST’ TRUCK FILLING CHUTE

- Hundreds of installations throughout Australia and Worldwide.

- Fully Australian made.

- Three (3) standard sizes:

-  M375 with 200mm Diam. Inlet

-  M560 with 300mm Diam. Inlet

-  M750 with 350mm Diam. Inlet

Each size available for	-	Open truck loading

-	Enclosed truck loading

-	Open and Enclosed truck loading

-	Extension length from 1m to 5m

Special chute with larger diameters and longer extension lengths are available.

Standard Features:

- Neoprene coated, wear resistant boot material ensures long life.

- Tilt switches level probe to control the loading.

- Slack cable limit switches and rotary limit switches to control the extension length.

- Automatic self-raising for open truck type.

- All hardware components are rust proofed or in stainless steel to ensure long life.

- Housing is sandblasted and powder coated with epoxy paint to protect against corrosion.

Optional Features:

- Internal Telescopic cones or cylinders for long extension spouts.

- High temperature resistant boot material.

- Bottom shut off cone to prevent product dribbling when chute is raised.

- Pneumatic or electric vibrators.

- Various types of level sensing to suit special loading product.

- Pneumatic thrower for single hatch container.

- Integral filter with dust extraction fan.

(KOO-13-005/0505)